## Slide 1
ZAGAZIG UNIVERSITY • FACULTY OF COMPUTERS AND INFORMATICS
Artificial Intelligence and Data Science Program
Health Mate
An AI-Assisted Remote Monitoring System for Chronic Cardiovascular Care
GRADUATION PROJECT TEAM
Omar Ashraf Mohamed Kamal (Team Leader) • Seif EL-Deen Amr Mohamed
Rofida Mohamed Ahmed Ibrahim • Farida Abdelazim Gharib Mohamed
Supervised by Ass. Prof. Dr. Amr Abdellatif & Eng. Mohamed Ameen 2025 – 2026

## Slide 2
ROADMAP
What We'll Cover in the Next Few Minutes
01
The Problem
The silent killer, and an invisible caregiver gap
02
The Market Today
What's out there — and why it isn't enough
03
Our Solution
One coherent system: app + backend + AI + hardware
04
Architecture & Data
How it's actually built, end to end
05
Custom IoT Hardware
A cuffless BP sensor and a smart medicine box
06
Two AI Models
Cuffless blood pressure & symptom triage — results and limitations
07
The Experience
A walkthrough of the real, running app
08
Impact & What's Next
Who benefits today, and the road ahead
Health Mate • Zagazig University — 2025/2026
1

## Slide 3
THE PROBLEM — “THE SILENT KILLER”
Hypertension has no symptoms —
until it becomes an emergency.
The World Health Organization calls hypertension “the silent killer” for exactly this reason: most people with high blood pressure feel completely normal, right up until a stroke, heart attack, or kidney failure.
Snapshot vs. Trend
A clinic visit captures one moment. Disease progression is a trend across weeks, not a single number.
Patients Skip Readings
Cuff placement, sitting still, remembering to log — any one step failing means a missed reading.
Caregivers Are Blind
Family caregivers have no channel to the data unless told directly. They can only react, never notice.
Health Mate • Zagazig University — 2025/2026
2

## Slide 4
WHY CURRENT CARE FALLS SHORT
Two Failure Modes, Recurring Constantly
Patient side
● Correct cuff placement is easy to get wrong
● Sitting still for an accurate reading takes discipline
● Remembering a daily schedule, unassisted, is unreliable
● Medication doses are just as easy to forget or misplace
Caregiver side
● No channel to the patient's data short of phoning and asking
● Can only react to what they are told — often after the fact
● No automatic warning when a reading crosses a dangerous line
● No way to reach the patient quickly during a real emergency
THE SILENT KILLER, BY THE NUMBERS
1.28 B
adults worldwide live with hypertension (WHO)
46%
don't know they have it — no symptoms until it's serious
10 M+
deaths every year from uncontrolled blood pressure
Source: WHO Global Report on Hypertension, 2023 / 2025
Health Mate • Zagazig University — 2025/2026
3

## Slide 5
THE MARKET TODAY
How This Is Solved Right Now
Traditional Cuff + Paper Log
Manual measurement, manual logging. Cheap and accurate, but entirely dependent on patient discipline and memory.
Consumer Wearables
(e.g. Omron HeartGuide)
A cuff built into a wristwatch. FDA-cleared and convenient, but still a cuff, and still no caregiver-facing safety net.
Connected Home Monitors
(e.g. Withings BPM Connect)
Automated Wi-Fi upload of cuff readings to an app. Great trend logging, but no cuffless sensing and no clinical triage layer.
Clinical RPM Platforms
Care-team dashboards for chronic conditions. Powerful for providers, but built around clinical staff — not a family caregiver.
All four share the same gap: none combine cuffless sensing, AI-driven safety alerts, and a built-in family-caregiver channel in one system.
Health Mate • Zagazig University — 2025/2026
4

## Slide 6
COMPARISON
Health Mate vs. the Market
Capability | Traditional Cuff + Log | Consumer Wearables | Connected Home Monitors | Clinical RPM Platforms | Health Mate
Cuffless AI-based sensing | ✗ | ✗ | ✗ | ✗ | ✓
Live caregiver linking + alerts | ✗ | △ | △ | △ | ✓
Symptom / red-flag triage engine | ✗ | ✗ | ✗ | △ | ✓
Smart medication reminder hardware | ✗ | ✗ | ✗ | ✗ | ✓
Built-in emergency calling | ✗ | ✗ | ✗ | ✗ | ✓
Full Arabic + English parity | ✗ | ✗ | ✗ | △ | ✓
Clinically validated / cleared | ✓ | ✓ | ✓ | ✓ | Research prototype
△ = partial / not designed for this use case • Based on each product's public specifications; Health Mate is an unvalidated graduation-project prototype.
Health Mate • Zagazig University — 2025/2026
5

## Slide 7
OUR ANSWER
Solve Both Halves Together —
Not Separately.
A cuffless sensor and a family health-sharing app already exist separately elsewhere. The distinctive bet here: fuse sensing, AI safety, and caregiver visibility into one system.
BP Sensing Unit
ESP8266 + MAX30102 PPG + AD8232 ECG — no cuff
1
FastAPI Backend
Every clinical decision + 2 trained AI models
2
Smart Medicine Box
ESP32 + LEDs + buzzer — adherence indicator
3
Flutter Mobile App
One shared codebase: patient & caregiver views
4
Note: the BP sensing unit and the smart medicine box are two independent devices — they never talk to each other, only to the backend.
Health Mate • Zagazig University — 2025/2026
6

## Slide 8
PRODUCT AT A GLANCE
What a Patient and a Caregiver Can Actually Do
Patient
● Guided, 8-second cuffless BP measurement
● Manual entry + calibration against a cuff reading
● Medication catalog with smart-box drawer assignment
● Structured symptom assessment with urgency triage
● One-tap audio/video call to a linked caregiver
● Full experience in Arabic or English, RTL included
Caregiver
● Live view of a linked patient's BP, risk tier & history
● Automatic alert on a high or critical reading
● Medication adherence visibility, not just reminders
● Notification if a patient's calibration drifts or goes stale
● Direct call-back to the patient in a concerning moment
● Can monitor more than one linked patient at once
Both sides connect through one shared, AI-monitored backend — the same reading that reassures a patient is the one that can alert their caregiver.
Health Mate • Zagazig University — 2025/2026
7

## Slide 9
SYSTEM CONTEXT
Two Actors, One Shared App, One Backend of Record
Patient
Caregiver
Flutter Mobile App
patient & caregiver UI
FastAPI Backend
every clinical decision
+ 2 AI models
BP Sensing Unit
ESP8266
Smart Medicine Box
ESP32
REST
+ WS
→
HTTP
POST
activate
The hardware never makes a clinical decision — signal validation, model inference, calibration and alerting all run in the backend, not on the devices themselves.
Note: the BP unit and the smart medicine box never talk to each other directly — both are independent, reporting only to the backend.
Health Mate • Zagazig University — 2025/2026
8

## Slide 10
SOFTWARE ARCHITECTURE
Four Layers, Two Architectural Styles
Service-layer style (most of the system)
● Auth, medications, vitals, notifications, contacts, calls, IoT
● Routers → flat services → SQLAlchemy models, wired via Depends()
● Simple, direct, easy to trace end to end
Clean / hexagonal architecture (symptom checker v2 only)
● Domain rule engine, application use-cases, infrastructure adapters
● Use-cases depend on interfaces, not concrete implementations
● Two chat-storage backends (Redis / in-memory) already prove the boundary works
Health Mate • Zagazig University — 2025/2026
9

## Slide 11
DATABASE DESIGN
21 Tables, One PostgreSQL System of Record
21
SQLAlchemy models
16+
Alembic migrations
1
many-to-many table
(patient ↔ caregiver)
A partial unique index enforces one active primary caregiver per patient — a real database-level rule, not just app logic.
Health Mate • Zagazig University — 2025/2026
10

## Slide 12
TECHNOLOGY STACK
What It's Actually Built With
Layer | Technologies
Mobile App | Flutter, Riverpod, Dio + Retrofit, Hive, flutter_secure_storage, easy_localization
Backend API | FastAPI (Python), Socket.IO (WebRTC signaling), APScheduler (reminders/alarms)
Data & Infra | PostgreSQL 15 + asyncpg, Redis, Cloudinary, Firebase Cloud Messaging
AI / ML | TensorFlow / Keras (BP model), LightGBM (symptom triage), scikit-learn baselines
IoT Firmware | ESP8266-12E (BP unit), ESP32 (smart medicine box), Arduino C++
Engineering | Docker Compose, Alembic migrations, 15 automated backend test suites
100%
containerized via Docker Compose
Async
I/O throughout the FastAPI backend
Type-safe
Dart mobile codebase end to end
Open-source
entire stack, no proprietary lock-in
Health Mate • Zagazig University — 2025/2026
11

## Slide 13
THE SHARED MOBILE APP
Same Data, Two Tailored Experiences
Patient Home
Caregiver Home
QR Patient ↔ Caregiver Linking
Health Mate • Zagazig University — 2025/2026
12

## Slide 14
CUSTOM IOT HARDWARE
Blood-Pressure Sensing Unit
Health Mate • Zagazig University — 2025/2026
13

## Slide 15
CUSTOM IOT HARDWARE
Firmware Built for Real Conditions, Not a Demo
What the firmware guarantees
● ESP8266-12E + MAX30102 (PPG) + AD8232 (ECG) — no on-device model
● Samples both channels at a precise 100 Hz, unaveraged, matching the trained model exactly
● Gates on finger + lead contact before accepting any sample — discards a bad window rather than sending it
● Retries uploads with exponential backoff; a 10-second heartbeat keeps device status current
Known Limitations
● The device authentication token shipped in this firmware is a hardcoded placeholder rather than a per-device provisioned secret — production deployment requires per-device credential issuance
● The hardware never runs the model, calibration, or risk logic — every clinical decision happens in the backend
● No accuracy numbers yet exist from real MAX30102/AD8232 recordings — every reported metric comes from the held-out test dataset
100 Hz
sampling rate, unaveraged
800
samples per channel per window
8 s
capture window per reading
≤500 ms
to discard a bad window
Health Mate • Zagazig University — 2025/2026
14

## Slide 16
CUSTOM IOT HARDWARE
Smart Medicine Box: Indicator, Not Dispenser
No motor, servo, or locking mechanism exists in the firmware — the box indicates the correct drawer via LED, and the patient opens it by hand.
● ESP32 + 74HC595 shift register driving up to 6 drawer LEDs, plus a buzzer
● The LED lights the correct drawer; the patient still opens it by hand
● Fail-soft: an unreachable box never blocks the phone notification for the same reminder
● Adherence is logged from the patient tapping “taken” in the app — not from any drawer-open sensor
● Still genuinely useful: it turns “time for a dose” into one unambiguous physical pointer
0
motors or locks
6
max drawers supported
Fail-soft
always
Health Mate • Zagazig University — 2025/2026
15

## Slide 17
THE AI CORE
Two Purpose-Built Models,
Compared Fairly.
Not a single black box — two independent problems, each benchmarked against multiple baseline alternatives.
Cuffless Blood-Pressure Model
650,000+ signal windows from a MIMIC-derived dataset • 10 models compared: 6 classical + 4 deep learning • Estimates SBP/DBP from 8s of PPG+ECG
Symptom-Triage Model
232-dimensional structured feature vector • Severity, duration, age, vitals & risk factors — not bag-of-words • Backed by an escalate-only safety rule engine
The two models are otherwise independent — they connect at exactly one point: a high or critical BP reading can offer an optional symptom follow-up, feeding the same triage engine (shown ahead).
Health Mate • Zagazig University — 2025/2026
16

## Slide 18
BLOOD-PRESSURE MODEL
Why Estimating BP Without a Cuff Is Hard
The Physiology
Pulse transit time — the delay between an ECG R-peak and the matching PPG pulse — shortens as arterial pressure rises. It's the classical basis for cuffless estimation.
The Signal
An 8-second, 800-sample window of PPG + ECG at 100 Hz has to be turned into two numbers: systolic and diastolic pressure.
The Catch
The PTT-to-pressure relationship is nonlinear and patient-dependent — a well-known hard problem in biomedical signal processing, easy to overfit to one dataset.
Health Mate • Zagazig University — 2025/2026
17

## Slide 19
BLOOD-PRESSURE MODEL — METHODOLOGY
A Rigorous, Record-Level Fair Comparison
653,015
total signal windows
1,631
held-out patient records
10
models trained & compared
21
hand-crafted waveform features
● Record-level split (train/val/test) — not window-level — so overlapping windows from the same patient never leak across splits
● Bandpass filter → z-score normalize → feature extraction: the exact same code runs in training and in the production backend
Health Mate • Zagazig University — 2025/2026
18

## Slide 20
BLOOD-PRESSURE MODEL
21 Hand-Crafted Signal Features
Category | # | Examples
Heart rate & rhythm | 3 | HR (bpm), RR interval mean / std
Pulse transit time | 2 | PPG-peak minus preceding ECG R-peak
PPG waveform shape | 7 | Rise time, amplitude, mean/std/skew/kurtosis
PPG derivatives | 4 | 1st (velocity) & 2nd (acceleration) plethysmogram
ECG waveform | 5 | RR interval, QRS width, mean / std
Pulse transit time and heart rate carry the strongest linear correlation with SBP/DBP among the 21 features — but no single hand-crafted feature is strong enough alone, which is exactly why the raw waveform matters too.
Health Mate • Zagazig University — 2025/2026
19

## Slide 21
BLOOD-PRESSURE MODEL
Handling Imbalance Without Throwing Data Away
● Hypertension & Hypotension windows dominate the dataset; Normal & Elevated are comparatively rare
● A prior attempt downsampled to force balance — it discarded most of the data and made results worse (SBP MAE 11.47 vs. 9.13)
● Current approach: inverse-frequency sample weights (capped at 5×) — every real window is kept
● A modest 15% synthetic augmentation (noise, baseline wander, amplitude scaling) tops up the real data, not replaces it
Health Mate • Zagazig University — 2025/2026
20

## Slide 22
BLOOD-PRESSURE MODEL
Ten Models, One Clear Winner
Model | SBP MAE | DBP MAE | DBP BHS
1D-CNN (best) | 9.08 | 4.91 | B
TCN | 9.79 | 5.31 | B
TCN+BiLSTM+Attn (ours) | 10.17 | 5.63 | B
BiLSTM | 14.34 | 7.28 | C
XGBoost (best classical) | 14.71 | 7.45 | C
Ridge (weakest) | 18.03 | 8.59 | D
The team's own purpose-built architecture (TCN+BiLSTM+Attention) did not win — a plain 1D-CNN did. More complexity did not translate into better accuracy on this dataset.
Health Mate • Zagazig University — 2025/2026
21

## Slide 23
BLOOD-PRESSURE MODEL — RESULTS
Best ≠ Clinically Acceptable — Both Are True
9.08 mmHg
SBP MAE — Grade D, fails AAMI
4.91 mmHg
DBP MAE — Grade B, PASSES AAMI
80 ms
model inference time (of an 8s window)
Health Mate • Zagazig University — 2025/2026
22

## Slide 24
BLOOD-PRESSURE MODEL — CLINICAL EVALUATION
Predicted vs. Actual, Over Time
R² = 0.671
SBP — predicted tracks the true value over time
R² = 0.546
DBP — predicted tracks the true value over time
Health Mate • Zagazig University — 2025/2026
23

## Slide 25
BLOOD-PRESSURE MODEL
What's Still Open
● Every model in the study fails AAMI for SBP — treated as an indicative trend, not a diagnostic-grade number
● Trained and evaluated on ICU arterial-line data (MIMIC) — not yet on an ambulatory, home-use population
● No accuracy numbers yet from real MAX30102/AD8232 hardware recordings
This is a validation gap, not an integration gap: the firmware, backend inference, and calibration pipeline are all wired together end to end — what's missing is a measured accuracy number from real sensor hardware on a live subject.
Health Mate • Zagazig University — 2025/2026
24

## Slide 26
PER-PATIENT CALIBRATION
Adapting the Model to One Specific Person
● Fewer than 8 cuff-vs-model samples → robust median offset only
● 8 or more samples → upgrades to a full least-squares linear fit
● Scale clamped to [0.70, 1.30], offset to [−25, +25] mmHg — a bad fit can't run away
● A separate scheduled job detects drift (>8 mmHg SBP / >5 mmHg DBP shift) or staleness (>90 days), prompting recalibration
Health Mate • Zagazig University — 2025/2026
25

## Slide 27
SYMPTOM-TRIAGE MODEL
Two Generations, Both Still Live Today
Aspect | v1 — Legacy | v2 — Structured (production)
Input | Free text or a flat symptom list | Severity, duration, age, vitals, conditions
Representation | TF-IDF vectorizer | 232-dimensional engineered feature vector
Model | Best of 5 classical candidates | LightGBM, 40 disease classes
Safety logic | None beyond the model's own output | Dedicated rule engine, escalate-only
A free-text / TF-IDF model has no slot to weigh “a mild headache for 2 days” differently from “a severe headache for 2 weeks.” v2 exists precisely to fix that — a genuinely different representation, not a tuning pass on v1. Both remain reachable in the app today.
v1
Free text
TF-IDF vectorizer
→
v2
Structured wizard
232-dim feature vector
→
+
Safety-first
rule engine (escalate-only)
Health Mate • Zagazig University — 2025/2026
26

## Slide 28
SYMPTOM-TRIAGE MODEL
232 Dimensions Built for Nuance
Segment | Size | Content
Symptom presence | N | Multi-hot: 1 if the symptom was selected
Symptom severity | N | 0 if absent, else reported severity
Duration bucket | 4 | <1, 1–3, 4–7, >7 days (one-hot)
Age group | 3 | Child / adult / elderly (one-hot)
Risk factors | 5 | Hypertension, diabetes, asthma, hypothyroidism, CKD
Vitals | 4 | Normalized SBP/DBP/HR + a vitals-present flag
Synthetic, on purpose
● 9,840 train / 2,460 test cases generated from a symptom-taxonomy profile per disease
● Every case's urgency label comes from the real rule engine — the dataset can never disagree with production logic
● Confusable pairs (Cold/Flu/COVID-19, Hypertension/Migraine/Stroke) were specifically targeted
9,840
training cases
2,460
held-out test cases
40
disease classes covered end to end
Health Mate • Zagazig University — 2025/2026
27

## Slide 29
SYMPTOM-TRIAGE MODEL — RESULTS
Strong Overall, With Room to Improve
85.8%
top-1 accuracy
95.5%
top-3 accuracy
0
cross-confusion in targeted disease pairs
40
disease classes
Weakest classes (top-1 accuracy) | Score
Myocarditis | 0.350
Hypertrophic cardiomyopathy | 0.400
Coronary artery disease | 0.517
Congestive heart failure | 0.600
Ventricular tachycardia | 0.650
● Almost every weak class is a cardiac subtype — exactly the specialty this project is built around
● Logistic Regression (0.870) and Random Forest (0.866) both score higher than the deployed LightGBM (0.858) on the identical dataset
Health Mate • Zagazig University — 2025/2026
28

## Slide 30
THE SAFETY NET
A Rule Engine That Can Only Escalate — Never Suppress
1. Red Flags
Certain symptoms (e.g. syncope) trigger regardless of the ML model's own confidence
→
2. Vitals Floor
SBP/DBP/SpO2 thresholds set an urgency floor, shared with the BP-alerting feature
→
3. Urgency Level
Critical / High / Moderate / Low — combining red flags, vitals, and the model
→
4. Caregiver Alert
High or Critical urgency can trigger an immediate caregiver notification
The ML model's prediction is never allowed to override a rule-engine red flag downward — a hard, explicit design rule enforced in code, not a soft guideline.
WHERE THE TWO AI MODELS ACTUALLY CONNECT
High / Critical
BP reading
→
Patient offered a
quick symptom check
→
Feeds the same
urgency engine
Health Mate • Zagazig University — 2025/2026
29

## Slide 31
THE PROJECT'S BIGGEST LESSON
Architectural complexity
must earn its place.
It does not, by default, beat a simple baseline that is actually run — the same pattern appeared independently in both AI systems built for this project.
Blood Pressure
A plain 1D-CNN beat the team's own TCN + BiLSTM + Attention model, purpose-built for this exact task.
SBP MAE: 9.08 (1D-CNN) vs. 10.17 (ours)
Symptom Triage
Logistic Regression outscored the LightGBM model actually chosen for production, on the identical dataset.
Accuracy: 0.870 (LogReg) vs. 0.858 (LightGBM)
Health Mate • Zagazig University — 2025/2026
30

## Slide 32
THE EXPERIENCE
Guided Blood-Pressure Measurement, Step by Step
1. Setup — live sensor status
2. Measuring — 8s capture
3. Result — risk tier shown
4. History — trend, not a snapshot
Health Mate • Zagazig University — 2025/2026
31

## Slide 33
THE EXPERIENCE
Medication Management & the Smart Box
1. Medication list
2. Add / edit a medicine
3. Assign a smart-box drawer
4. Full-screen dose alarm
Health Mate • Zagazig University — 2025/2026
32

## Slide 34
THE EXPERIENCE
The Structured Symptom-Checker Wizard
1. Category
2. Symptoms
3. Severity
4. Result & urgency
Health Mate • Zagazig University — 2025/2026
33

## Slide 35
THE EXPERIENCE
Emergency Calling, Built In
Outgoing call
Incoming call
Active call
Emergency call action
Health Mate • Zagazig University — 2025/2026
34

## Slide 36
THE EXPERIENCE
The Notifications Inbox
Every alert, in one place
● Medication reminders and confirmations
● BP risk-tier alerts sent to a linked caregiver
● Calibration drift / staleness prompts
● Symptom-checker urgency notifications
● Read / unread state, oldest to newest
How Alerts Are Delivered
● Firebase Cloud Messaging push, plus a persistent in-app inbox
● Caregiver BP alerts respect a cooldown — 15 min for critical, 30 min for high — so one event never floods them
● Read / unread state persists per user across devices
Health Mate • Zagazig University — 2025/2026
35

## Slide 37
BUILT FOR EVERYONE
Bilingual and Offline-First, Not as an Afterthought
613 / 614
English / Arabic translation keys — near 1:1 parity
100%
of reminders & alerts localized, not just static text
Hive
offline cache for last-known BP reading & history
● Full right-to-left layout for Arabic — a first-class concern in the codebase, implemented at the translation-key level
● Risk levels (Normal/Low/Moderate/High/Critical) are computed once in the backend as plain strings — the UI decides how to translate and display them, never the reverse
● Reminders keep firing locally without connectivity; the last known BP reading and history stay visible offline
English → left to right
Home > Vitals > BP History
العربية ← right to left
سجل ضغط الدم < المؤشرات < الرئيسية
Health Mate • Zagazig University — 2025/2026
36

## Slide 38
IMPACT
Who We Built This For
Elderly Hypertension Patients
Large, simple UI and a guided sensor flow that removes every step they could get wrong, in their own language.
Any Long-Term Hypertension Patient
Continuous history instead of clinic snapshots, with automatic caregiver escalation on a critical reading.
Memory-Impaired Patients
The smart box turns “time for a dose” into one unambiguous physical pointer at a single drawer.
Health Mate • Zagazig University — 2025/2026
37

## Slide 39
RELIABILITY
What Works, What's Left
What we hardened
● Hardware fails soft — a missing model or unreachable device degrades, never crashes
● Dedicated unit tests on the newest, safety-relevant code: the rule engine, BP endpoints, calibration/drift
● Every clinical output is clamped to a physiologically plausible range before it reaches a screen
● Automated test scans for Arabic text-encoding corruption — a real, previously-seen bug class
What's Still Open
● Session/token revocation isn't implemented — a standard stateless-JWT tradeoff
● The caregiver-linking QR code carries a plain, unencrypted user ID
● /iot/sensors/* always returns simulated data, regardless of mode — it should not be read as live telemetry
● Test coverage is concentrated on the newest BP/symptom-checker work, not spread evenly across the codebase
15
automated backend test suites
0
crashes from a missing model/device
2
known open gaps, disclosed above
Health Mate • Zagazig University — 2025/2026
38

## Slide 40
RESULTS THAT MATTER
The Project at a Glance
4.91 mmHg
DBP MAE — clears AAMI
85.8% / 95.5%
symptom-triage top-1 / top-3
21
database tables, 1 backend of record
2
custom IoT devices, built from scratch
653K+
signal windows across 1,631 patients
15
automated backend test suites
613/614
EN/AR translation-key parity
0
cross-confusion in targeted disease pairs
Health Mate • Zagazig University — 2025/2026
39

## Slide 41
KNOWN RISKS & LIMITATIONS
The Risk Register
Risk | Severity
SBP estimation fails the clinical AAMI standard | High
Symptom checker weakest on cardiac subtypes — the project's own focus | High
No server-side session / refresh-token revocation | Medium
Caregiver-linking QR code is an unencrypted user ID | Medium
BP model not yet validated against real sensor hardware | Medium
Severity reflects how directly each risk affects the core clinical claim or production-readiness — each maps to a mitigation on the roadmap that follows.
2
high-severity risks
3
medium-severity risks
5
tracked risks, each with a mitigation path
Health Mate • Zagazig University — 2025/2026
40

## Slide 42
ROADMAP AHEAD
What Comes Next
Validate against reality
● Collect real MAX30102/AD8232 recordings against reference cuff readings
● Re-run the calibration study using samples genuinely separated in time, matching how the deployed service actually collects them
● Investigate why the attention-based model underperformed the simpler 1D-CNN
Harden for production
● Server-side session/refresh-token revocation
● Sign, encrypt or expire the caregiver-linking QR payload
● Clinical sign-off on the one still-unsigned BP threshold in the triage rules
● Unify the two symptom-checker generations behind one entry point
HOW WE GET THERE
Now
Working prototype
→
Next
Real-hardware validation
→
Then
Security hardening
→
Goal
Clinical sign-off
Health Mate • Zagazig University — 2025/2026
41

## Slide 43
CONCLUSION
Health Mate, in One Slide
A working, end-to-end remote-monitoring system spanning custom sensor hardware, two independently trained AI models, and a backend that centralizes every clinical decision — built and evaluated end-to-end, from firmware to trained models.
4.91 mmHg
DBP MAE — clears AAMI
85.8% / 95.5%
symptom-triage accuracy
21 tables / 4 layers
one coherent, working system
Every number in this deck is measured directly from the code and data, and every limitation is disclosed deliberately.
Health Mate • Zagazig University — 2025/2026
42

## Slide 44
Thank You
Questions & Discussion
HEALTH MATE TEAM
Omar Ashraf Mohamed Kamal • Seif EL-Deen Amr Mohamed
Rofida Mohamed Ahmed Ibrahim • Farida Abdelazim Gharib Mohamed
Supervised by Ass. Prof. Dr. Amr Abdellatif & Eng. Mohamed Ameen